## Slide 1: Australian ExpressRoute
Overview of Technical connection

## Slide 2: Connectivity choices: Internet or Private
Cloud on your WAN
  Traffic flows directly from customer WAN to Microsoft
  Reduces complexity
  Lower latency, higher bandwidth and higher availability
Microsoft
WAN
Corp HQ
Branch office 1
Branch office 2
Public internet
IPsec VPN over Internet
  Encrypted data traverses Internet to reach Azure
  Limited bandwidth and higher availability
Microsoft
WAN
Corp HQ
Branch office 1
Branch Office 2
Public internet

## Slide 3: ExpressRoute
Microsoft
WAN
Corp HQ
Branch office 1
Branch office 2
Public internet
ExpressRoute provides a private, dedicated, high-throughput network connection to Microsoft
Security
Lower cost
Predictable performance
High throughput

## Slide 4: ExpressRoute Connectivity
Microsoft Edge
Customer’s network
Customer’s connection
Partner Edge
Traffic to public IP addresses in Azure
Traffic to Virtual Networks
Traffic to Office 365 Services

## Slide 5: Huge infrastructure scale is the enabler
24 Regions Worldwide, 19 ONLINE…huge capacity around the world…growing every year
  100+ datacenters
  Top 3 networks in the world
Operational
Announced/Not Operational
Central US
Iowa
West US
California
North Europe
Ireland
East US
Virginia
East US 2
Virginia
US Gov
Virginia
North Central US
Illinois
US Gov
Iowa
South Central US
Texas
Brazil South
Sao Paulo
West Europe
Netherlands
China North *
Beijing
China South *
Shanghai
Japan East
Saitama
Japan West
Osaka
India South
Chennai
East Asia
Hong Kong
SE Asia
Singapore
Australia South East
Victoria
Australia East
New South Wales
  * Operated by a regional partner
India Central
Pune
Canada East
Quebec City
Canada Central
Toronto
India West
Mumbai

## Slide 6: Billing options and bandwidths
Connectivity Provider
New billing options
‘Unlimited Data’ – Fixed Monthly Price
‘Metered Data’ – Variable Monthly Price
1 Gbps
2 Gbps
5 Gbps
10 Gbps
50 Mbps
100 Mbps
200 Mbps 500 Mbps
Bandwidth | Billing Model | 
 | Unlimited Data | Metered Data
10 Mbps |  | 
50 Mbps |  | 
100 Mbps |  | 
200 Mbps |  | 
500 Mbps |  | 
1 Gbps |  | 
2 Gbps |  | 
5 Gbps |  | 
10 Gbps |  | 
You pick the billing model that works for you.
No more EXPs and NSPs!

## Slide 7: ExpressRoute connectivity models
Cloud Exchange Co-location
ExpressRoute
Point-to-point Ethernet Connection
ExpressRoute
Any-to-any (IPVPN) Connection
ExpressRoute
WAN

## Slide 8: ExpressRoute Sites and Partners
Atlanta
Chicago Chicago (Gov Cloud)*
Dallas
LA
NY
Seattle
Silicon Valley
Washington DC
Washington DC (Gov Cloud)*
Sao Paulo
Amsterdam
Dublin*
London
Chennai*
Hong Kong
Mumbai*
Melbourne*
Osaka*
Singapore
Sydney
Tokyo

## Slide 9: ExpressRoute and S2S VPN Coexistence
ExpressRoute
S2S VPN as a backup for ExpressRoute
S2S connectivity to branch offices
Connecting Virtual Networks in other Azure regions
Contoso HQ
Exchange
AD/DNS
IIS Servers
SQL Farm
Monitoring
Contoso virtual networks/VMs
Internet
Services on public IPs
VPN Gateway
(Internet Edge)

## Slide 10: ExpressRoute Premium Add On
NEW
Global connectivity
  Link a Virtual Network from any Azure Region to your ExpressRoute circuit
More routes (IP prefixes)
  Supports up to 10,000 routes, increase from 4,000 routes
Connect more Virtual Networks
  Up to 100 virtual networks depending on bandwidth option

## Slide 11: VPN Gateways for Virtual Network
ExpressRoute gateway or VPN gateway needed to access a virtual network
Introducing a new Standard Gateway
  Supports ExpressRoute and VPN coexistence
  Improved throughput for ExpressRoute
NEW
Virtual Network Gateway SKU | ExpressRoute GW Throughput | VPN GW ExpressRoute Coexistence | VPN GW Throughput | VPN GW Max IPsec Tunnels | Cost (USD) / Hour
Basic | 500 Mbps | No | 100 Mbps | 10 | $0.04
Standard | 1000 Mbps | Yes | 100 Mbps | 10 | $0.19
Performance | 2000 Mbps | Yes | 200 Mbps | 30 | $0.49
Note that ExpressRoute traffic for Azure public services, O365, and Skype for Business does NOT go through a Virtual Network gateway

## Slide 12: Office 365 Timelines and Partners
Australian ER Partners with O365
  Other providers soon. (Telstra Q1 2016)
Supported Workloads
  Exchange Online & Exchange Online Protection
  SharePoint Online, OneDrive for Business, Office 365 Video, Delve
  Skype for Business Online (formerly Lync Online)
  Office Online
  Power BI and Project Online

## Slide 13: ExpressRoute Traffic Paths within Australia
Overview of Technical connection
http://azure.microsoft.com/en-us/services/expressroute/
https://azure.microsoft.com/en-us/documentation/articles/expressroute-faqs/

## Slide 14: 4 ExpressRoute partners in Australia:
ER Partner | Type of Connection | Connection Advantages
Telstra | Via Telstra Cloud Direct Connect (metered & unmetered) | Great for existing Telstra MPLS customers that want to connect multiple sites directly to Azure
Equinix | metered & unmetered | Great for Equinix customers (or that have connectivity to Equinix) that want to connect to multiple clouds with the same link(s)
NextDC | metered & unmetered | Great for NextDC customers (or that have connectivity to NextDC) that want to connect to multiple clouds with the same link(s)
MegaPort | metered & unmetered | Focuses on rapid (dynamic) provisioning of connectivity & bandwidth between major DCs, fully automated within minutes
Many connection paths (NOs & VNOs)
(Network Operators / Virtual Network Operators)
Most customers have telco connectivity to/from their head office & branch office(s) via a telco that is not directly connected to an ExpressRoute partner. As such, these telcos can include the ER service from one of the above providers into their end-to-end service and provide a complete capability to customers.

## Slide 15: Customer network components
MS Enterprise Edge
ER Provider
Physical Network Provider
ER Partners provide multi-tenancy, security for MS Connectivity
Datacentre
Microsoft’s high speed / enterprise cloud connection point
Microsoft carries all traffic from this point to Azure (an other MS cloud services) and return. This is included in the cost of the ER service.
ER provider secures connectivity for MS cloud connectivity
MS SLA’s apply (based on redundant connections)
Network Operators / Virtual Network Operators provide IP circuits to customers offices / datacentres
Customer internal LAN
Optional / required customer / partner network equipment (routers, etc…) for BGP peering, firewalls, etc…

## Slide 16: Azure Australia East (Sydney) Express Route Connectivity (existing)
MSEE
(Microsoft Enterprise Edge)
Optus MPLS
Customer Racks
Telstra MPLS
Customer Racks
Existing ER infrastructure
Customer ER traffic
Customer ER traffic
Azure Infrastructure
Customer ER traffic
ER connectivity available now
Sydney, Mascot
S1 – Macquarie Park
Customer ER traffic

## Slide 17: Azure Australia South East (Melbourne) Express Route Connectivity
MSEE
(Microsoft Enterprise Edge)
Optus MPLS
Customer Racks
Telstra MPLS
Customer Racks
Azure Infrastructure
M1 – Port Melbourne
Melbourne
Short 1.8 Km dedicated fibre (=direct cross connect)

## Slide 18: ExpressRoute Provider Partners in Australia (with direct connection to MS Enterprise Edge)
Name | Type | Connection Locations
Equinix | ER connection provider ECX – Equinix Cloud Exchange | Sydney - 47 Bourke Road, Alexandria, Sydney, NSW 2015 Melbourne - 600 Lorimer Street, Port Melbourne, Victoria 3207 http://www.equinix.com/services/interconnection-connectivity/cloud-exchange/
Telstra | Telstra Cloud Direct Connect | MPLS network connected via Sydney (Alexandria) & Melbourne (Port Melbourne)
NextDC | ER connection provider AXONVX | Melbourne - 826 Lorimer Street, Port Melbourne, Victoria 3207 http://www.nextdc.com/data-centres/services/microsoft-azure-expressroute-connections http://www.nextdc.com/axonvx-virtual-connectivity-demand
MegaPort | ER connection provider | https://www.megaport.com/ https://megaport.com/about/megaport_enabled_locations

## Slide 19: NATIONAL COVERAGE

## Slide 20: Connecting to Microsoft Azure
Microsoft Azure requires dual paths for redundancy
2 x Port Setup
2 x Port Rental
2 x Elastic Cross Connects
Plus connectivity from customer colocation rack (via cross connect) or from customer premises (via carrier service)
Customer
Top of Rack Switch
AXONVX Ports
Data centre
cross connects or
carrier service
AXONVX Switching Fabric
Elastic
Cross Connects
(EXC)

## Slide 21: Supporting multiple customers
Data Centre 1
Shared ports, individual elastic cross connects (EXC’s)
One interconnect, multiple customer connections
Rapidly provision circuits
Orchestrate your solutions with AXONVX APIs
Customer
Equipment
Systems Integrator
Multiple Customers

## Slide 22: MPLS WAN

## Slide 23: DARK FIBRE / ETHERNET

## Slide 24
Great web links for more information
  ExpressRoute Technical Documentation: https://azure.microsoft.com/en-us/documentation/services/expressroute/
  ExpressRoute for Office 365: https://support.office.com/en-us/article/Azure-ExpressRoute-for-Office-365-6d2534a2-c19c-4a99-be5e-33a0cee5d3bd
  Other related services
  Microsoft Cloud Services and Network Security:
  https://azure.microsoft.com/en-us/documentation/articles/best-practices-network-security.html
  Azure Virtual Networks: https://azure.microsoft.com/en-us/documentation/services/virtual-network/
  Network Security Groups: https://azure.microsoft.com/en-us/documentation/articles/virtual-networks-nsg/
  User Defined Routing: https://azure.microsoft.com/en-us/documentation/articles/virtual-networks-udr-overview/
  Azure Virtual Gateways: https://azure.microsoft.com/en-us/documentation/services/vpn-gateway/
  Site-to-Site VPNs: https://azure.microsoft.com/en-us/documentation/articles/vpn-gateway-site-to-site-create/
References
Notes: Most of these links are on the Azure.com website under the documentation heading covering many of the topics I've discussed today. There are links to Getting Started and How To’s that are very informative. Most of the examples we’ve seen today are from the bottom link, Microsoft Cloud Services and Network Security, a Best Practices white paper the link takes you to high level overviews, some of what we’ve covered today, and links to detailed instructions on how to build the each of the examples I’ve discussed today and more. The detailed examples use both the classic PowerShell scripting and the new ARM template methods.