## Slide 1: First-Hop Redundancy Protocol VRRP

## Slide 2: Virtual Router Redundancy Protocol
Like HSRP
  VRRP enable preemption by default
  VIP MAC uses same structure 0000.5e00.01xx (group)
  VRRP uses a multicast address 224.0.0.18
  VRRP uses IP protocol 112
  Default priority 100
Versions of VRRP
  VRRPv2: Supports IPv4
  VRRPV3: Supports IPv4 and IPv6

## Slide 3: Virtual Router Redundancy Protocol
Legacy Configuration of VRRP
  Supported only VRRPv2
INT GO/0/0
IP ADDRESS 192.168.1.254 255.255.255.0
VRRP 10 PRIORITY 110
VRRP 10 TIMERS ADVERTIES MSEC 100

## Slide 4: Virtual Router Redundancy Protocol
VRRP Election
  VRRP advertisement sent at 1 second intervals
  Based on Master/Backup
    The Master role can be the IP address of the interface
    The Master role can be the highest Priority number
    IT IS UP TO YOUR CONFIGURATION