## Slide 1: Switch Performance Issues

## Slide 2: Troubleshooting Switch issues
Tricky to troubleshoot
  Network is running slowly
  User expectation vs actual speed of the network
Test Network Performance
  To make sure that indeed the network is running slow
  Based on your baseline
If indeed there is an issue with a particular switch, isolated and troubleshoot it.

## Slide 3: Switch Troubleshooting Targets
Troubleshooting switches will be platform dependent
  Some similarities exist but not all are equal
Components to all switches:
  Ports or interfaces
  Forwarding logic: the hardware that makes the forwarding decisions based on different tables in the data plane
  Backplane: It physically interconnects switches' ports. (Ingress and Egress)
  Control Plane: CPU and Memory reside here. Responsible for running the switch’s operating system and building the needed structures used to make forwarding decisions.

## Slide 4: Switch Troubleshooting Targets

## Slide 5: Switch Troubleshooting Targets
Port Errors
  Check port statistics
    Excessive Frames
    TCP application is running slow
      TCP slow start
      Window size and bandwidth to be reduced
    Drop packets
    Use the show interface f0/1 counters
sw1#show interfaces gig 1/0/9 counters
Port InOctets InUcastPkts InMcastPkts InBcastPkts
Gi 1/0/9 3125148 20003 3179 1
Port OutOctets OutUcastPkts OutMcastPkts OutBcastPkts
Gi 1/0/9 18744149 9126 96 6

## Slide 6: Switch Troubleshooting Targets
Use the show interface f0/1 counters errors
sw1#show interfaces gig 1/0/9 counters errors
Port Align-Err FCS-Err Xmit-Err Rcv-Err UnderSize
Gi 1/0/9 0 0 0 0 0
Port Single-Col Multi-Col Late-Col Excess-Col Carri-sen Runts Giants
Gi 1/0/9 5603 0 5373 0 0 0

## Slide 7: Switch Troubleshooting Targets
Error Counter | Description
Align-Err | An alignment error occurs when frames do not end with an even number of octets, while simultaneously having a bad CRC. An alignment error normally suggest a Layer 1 issue.
FCS-Err | A FCS error occurs when a frame has an invalid checksum, although the frame has no framing errors. This error often points to a Layer 1 issue but also it could be a duplex mismatch
Xmit-Err | A transmit error occurs when a port’s transmit buffer overflows. A speed mismatch overh between Inbound and Outbound links often results in a transmit error.
Rcv-Err | A receive error occurs when a ports receive buffer overflows. Congestion in the backplane could have caused this error. More than likely is a duplex mismatch
UnderSize | An undersize frame is a frame with a valid checksum but a size less than 64 bytes. This issue suggest that a connected host is sourcing invalid frame sizes

## Slide 8: Switch Troubleshooting Targets
Error Counter | Description
Single-Col | This error occurs when a single collision occurs before a port successfully transmits a frame
Multi-Col | More than one collision occurs before a port successfully transmits a frame. High bandwidth utilization on an attached link or duplex mismatch
Late-Col | This error is a collision that is not detected until well after the frame has begun to be forwarded. Cable to long or mismatched duplex conditions
Excess-Col | This error occurs when a frame experiences 16 successive collisions, after which the frame is dropped.
Carri-Sen | Is a counter that is incremented when a port wants to send data on a half duplex link. It is due to the CSMA/CD procedure. Full duplex does not have this problem
Runts | A runt is a frame that is less than 64 bytes in size and has a bad CRC. Layer 1 issue or duplex mismatch
Giants | A frame greater than 1518 bytes that has a bad FCS. The NIC is usually the culprit.