## Slide 1: Protocols and Services

## Slide 2: Protocols on the Host to Host Layer
TCP | UDP
Sequenced | Unsequenced
Reliable | Unreliable
Connection-oriented | Connectionless
Virtual Circuit | Low Overhead
Acknowledgements | No Acknowledgments
Windowing flow control | No windowing or flow control of any type

## Slide 3: Protocols on the Host to Host Layer
TCP | UDP
telnet 23 | SNMP 161
SMTP 25 | TFTP 69
HTTP 80 | DNS 53
FTP 20, 21 | BooTPS/DHCP 67
HTTPS 443 | 
SSH 22 | 
POP 110 | 
NTP 123 | 
IMAP4 143 | 

## Slide 4: The IP protocol
There are two main reasons for internet layer’s existence
  Routing
  Providing a single network interface of the upper layers
Without this layer, application programmers would need to write “hooks” into every one of their applications for each different Network Access Protocol.
IP provides on single network interface for the upper layer protocols.
List of important protocols at the internet layer
  IP
  ICMP
  ARP

## Slide 5: IP Protocol
For now, understand that IP looks at each packet’s address. Then using a routing table, it decides where a packet is to be sent next, choosing the best path to send it upon.
IP receives segments from the Host to Host layer and fragments them into datagrams if necessary. IP then reassembles datagrams back into segments on the receiving side.
Each datagram is assigned the IP address of the sender and that of the recipient.
Routing decisions based on packets destination IP addresses

## Slide 6: Protocols & Protocol Numbers for IP
Protocol | Protocol Number
ICMP | 1
IP in IP (TUNNELING) | 4
TCP | 6
UDP | 17
EIGRP | 88
OSPF | 89
IPv6 | 41
GRE | 47
Layer 2 tunnel (L2TP) | 115