## Slide 1: Conditionally Matching BGP Communities

## Slide 2: BGP Communities
BGP communities provide capability for tagging routers and for modifying BGP routing policy.
BGP communities are an optional transitive attribute that can route from AS to AS
  Communities are a 32-bit number included in the route
    Range 0-4.2 billion
    Full 16-bit number (6553700)
    Two 16-bit number (100:100)
In order to use the newer format, you must type the following:
R2(config}#IP BGP-Community NEW-format

## Slide 3: BGP Communities
Well-Known Communities
  RFC1997: defines a set of global communities
  Range: 4,294,901760 to 4,294,967,195
Three common well-know communities
  Internet: advertised on the internet
  No_Advertise: Not advertises to any BGP peer (iBGP/eBGP)
  No_Export: Will not advertise communities for eBGP. Will advertise for iBGP
How to enable BGP community support
  neighbor 10.1.1.9 send-community both

## Slide 4: BGP Communities