## Slide 1: Computer Networks Devices and Services
Dr. Mohammad Adly

## Slide 2: Computer Networks Devices
Network Interface Card (NIC)
Hub
Switch
Access Point (AP)
Router

## Slide 3: Network Interface Card (NIC)
Network adapter
Interface between PC and the network cable
Resides in the motherboard of PC
Communicate with PC through the device driver
Contain transmitter/receiver (transceiver)
Wired or wireless (via antenna)

## Slide 4: HUB
Shares frames between machines
Number of ports to connect several machines
Work with full duplex communication
Mixture of speeds (10M, 100M, 1G,…)
Allows collisions

## Slide 5: Collisions
Hub is one collision domain
Hub is one broadcast domain.
Collisions make the network slow and congested

## Slide 6: CSMA/CD

## Slide 7: Switch
Forward and filter frames
Work with full duplex communication
Mixture of speeds
One broadcast domain
Each port is a separate collision domain
No collisions
No Sniffing

## Slide 8: Access Point (AP)
Connects machines wirelessly in LAN
Transmits frames in the air media
Links wireless part to wired infrastructure
One broadcast domain
One collision domain
Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA)

## Slide 9: Router
Redirects packets between networks
Works based on a routing table
Divides network into broadcast domains
Divides network into collision domains

## Slide 10: Computer Network (LAN) Services
Software Resources Centralization
  Files
  Databases
  Applications
Hardware Peripheral Sharing
  Printer
  Scanner
  Processor
  Storage

## Slide 11: Computer Network (WAN) Services
Web Services
  Web Browsing
  Web Searching
  Social Media
E-mail Exchanging
File Transfer
Voice Calls
Video Conferencing

## Slide 12: Thank you