## Slide 1: Quality of Service

## Slide 2: Introduction to QoS
QoS uses tools to manage four characteristics of network traffic.
  Bandwidth (Capacity of the link)
  Delay (One way or Round-trip delay)
  Jitter (Variation in Delay)
  Loss (Lost messages)
QoS should do what?
  Send all packets
  Prioritize traffic
  Discard Traffic

## Slide 3: Introduction to QoS
Network Latency
  Propagation delay (fixed)
    Time to travel from source to destination
    ISP SLA's can be analyzed for the MIN, MAX and AVG latency
  Serialization delay (fixed)
    Time to place all bits on link
    Faster link better
  Processing delay (fixed)
    Time to take packet input to output queue
    CPU, IP Packet switching mode and Router architecture
  Delay variation (variable)
    Same as Jitter

## Slide 4: Introduction to QoS
Packet Loss
  Result of congestion on an interface
    High speed links fixes the issue
    Implement QoS congestion avoidance and management
    Implement traffic policing to drop low-priority packets
    Implement traffic shaping to delay packets instead of dropping them
QoS Models
  Best Effort
  Integrated Services (IntServ)
  Differentiated Services (DiffServ)

## Slide 5: Introduction to QoS
QoS Models
  Best Effort
    No QoS, traffic does not require special treatment
  Integrated Services (IntServ
    Bandwidth reservation and to indicate that they require special QoS treatment
    Real Time Applications such as voice and video
    Drawback, it cannot scale well on large networks (RSVP sent to network)
  Differentiated Services (DiffServ)
    Network identifies classes that require special QoS treatment
    No need for signaling protocol and no RSVP
    Highly Scalable
    End to End QoS solution
    Divides traffic into classes and Marks