## Slide 1: Spanning Tree Protocol Migration

## Slide 2: Review on STP
Original STP
  IEEE 802.1D
  Supports redundancy in a layer 2 network
  Keeping a loop-free topology
Features of STP
  Portfast
  BPDU Guard
  BPDU Filter
  Root Guard
  Loop Guard

## Slide 3: Migrating to Rapid-PVST+
Rapid-PVST+ most optimal type of STP to run
Faster convergence, normally less than 1 second
Each VLAN can run its own instance of STP
Rapid-PVST+ is backward compatible with 802.1D
Rapid-PVST+ holds the same features but the following can be removed:
  UplinkFast
  BackboneFast

## Slide 4: Syntax to Migrate to Rapid-PVST+
(config)#spanning-tree mode rapid-pvst
(config)#no spanning-tree uplinkfast
(config)#no spanning-tree backbonefast

## Slide 5: Migrating to Rapid-PVST+
Good to know information; here is a list of the features that still function in the Cisco Catalyst Switch being migrated to RPVST+
Portfast
BPDU Guard
BPDU Filter
Root Guard
Loop Guard