## Slide 1: Using Standard ACL’s

## Slide 2: Using a Standard ACL
Configuration types
Both serve the exact same purpose, deny a particular host
RX(config)#access-list 1 deny host 192.168.1.1
RX(config)#access-list 1 permit any
RX(config)#access-list 1 deny 192.168.1.0 0.0.0.0
RX(config)#access-list 1 permit any

## Slide 3: Using a Standard ACL
Configuration types
Both serve the exact same purpose, deny a particular network
RX(config)#access-list 1 deny 192.168.1.0 0.0.0.255
RX(config)#access-list 1 permit any
RX(config)#access-list 1 deny 192.168.1.16 0.0.0.15
RX(config)#access-list 1 permit any

## Slide 4: Using a Standard ACL
Configuration types
Both serve the exact same purpose, deny or permit VTY access
RX(config)#access-list 1 permit 172.16.1.0 0.0.0.255

## Slide 5: Applying a Standard ACL
Configuration types
Applying an ACL to an Interface
RX(config-if)#ip access-group 1 out
Applying an ACL to the VTY lines
RX(config-line)#ip access-class in