## Slide 1: The HSRP Redundancy Protocol

## Slide 2: Understanding Down HSRP
Redundancy is not only needed but required in an Network.
  How fast can the fail over happen?
  How is the client aware to switch?
  What if a WAN link fails?
HSRP
  Cisco proprietary protocol
  Uses by default hello timers of 3 seconds
  Hold timers are 10 seconds

## Slide 3: Breaking down HSRP
Gateways are organized into standby groups
One is active, and the other is Standby
Virtual router ID and MAC address is generated
VIP IP: 10.1.1.1
VIP MAC: 0000.0c07.ac01
  0000.0c = cisco vendor ID
  07.AC = HSRP ID
  X.X = Standby group number

## Slide 4: HSRP configuration
Active Router
  Int f0/0
  Standby 1 ip 10.1.1.1
  Standby 1 priority 120 (default is 100) Range is 0 -255
  Standby 1 preempt: Overthrow lower priority routers
  Standby 1 track f0/1
  Standby 1 timers msec 150 msec 700 (CAREFUL PROCESSOR CYCLES)

## Slide 5: Client configurations
All clients will have to be configured with the VIP, so when the Active router goes down they know to switch over to the other.
NO ARP FROM ACTIVE ROUTER, GOTO STABDY ROUTER.