## Slide 1: Welcome to OSPF

## Slide 2: All about OSPF
Link State Routing Protocol
Uses the Dijkstra Algorithm
Uses Cost
Based on Areas
Uses a Process ID Number
Configurations include
  Single area and Multi-Area
Uses Designated Routers and Backup Designated Routers

## Slide 3: All about OSPF
No limitation on routers
Does not summarize automatically
Uses Hello and Dead timers
Creates the following tables
  Routing table
  Neighbor table
  Database table

## Slide 4: All about OSPF
Term | Definition
LSDB | The data structure held by an OSPF router for the purpose of storing topology data
SPF | The name of the algorithm OSPF uses to analyze the LSDB
LSU | The name of the OSPF packet that holds the detailed topology information.
LSA | The name of class of OSPF data structures that hold topology information.
Area | Contiguous grouping of routers and router interfaces.
ABR | A router that has interfaces connected to at least two different OSPF areas.
Backbone Router | Any router that has a t least one interface connected to the backbone area.
Internal Router | A router that has interfaces connected to only one area, making the router completely internal to that one area.
DR | On a multi-access data links like LANs an OSPF router elected by the routers on that data link to perform special functions.
BDR | A router on a multi-access data link that monitors the DR and becomes prepared to take over for the DR, if it fails.

## Slide 5: OSPF Authentication Types
OSPF Authentication Type | Description
Type 0 | No authentication
Type 1 | Plain text authentication
Type 2 | Hashing authentication

## Slide 6: Authentication Configuration
Plain text authentication
R1 Int g0/1
ip ospf message-digest-key 1 md5 Spiderman
Router ospf 1
area 0 authentication message-digest
R2 Int g0/2
ip ospf message-digest-key 1 md5 Spiderman
ip ospf authentication message-digest

## Slide 7: Requirements to create Neighbors
Requirement | Yes/No
Interfaces primary IP addresses must be in same subnet | Yes
Must not be passive on the connected interface | Yes
Must be in same area | Yes
Hello and Dead timers must be the same | Yes
Router ID must be unique | Yes
Must pass neighbor authentication (Optional) | Yes
K-values must match | N/A

## Slide 8: Becoming Neighbors Detail
- Hello Sent from R1 to R2 (down state)
- Hello Received on R2 (init state)
- Hello Reply to R1 (2way state)
- Routers begin to exchange LSDB/DBD (exstart state)
- DBD's Acknowledged (loading state)
-LSRequest
-LSupdates (one router at a time)
- Once both routers know about all the routes.
(Full State)
NOW OSPF CAN BEGIN SPF CALCULATIONS