## Slide 1: Wireless Regulatory Bodies

## Slide 2: Agencies Governing Wireless Standards
Agency | Purpose
Institute of Electrical and Electronic Engineers | Creates and maintains operational standard
Federal Communications Commissions | Regulates the use of wireless device in the U.S.
European Telecommunications Standards Institute | Chartered to produce common standards in Europe
Wi-Fi Alliance | Promotes and test WLAN interoperability
It is important to understand what each of these agencies responsibilities are, since they are the ones that regulate wireless communications.

## Slide 3: Unlicensed Bands
ISM Band
  900MHz
    902.000 – 928.000MHz
  2.4 GHz
    2.4 – 2.4835GHz
UNII Band
  5GHz
    UNII-1: 5.15 – 5.25GHz
    UNII-2: 5.25 – 5.35GHz
    UNII-3: 5.75 – 5.825GHz

## Slide 4: IEEE Wireless Standards
Committee | Purpose
IEEE 802.11a | 54Mbps, 5GHz standard
IEEE 802.11b | Enhanced to 802.11 to support 5.5/11Mbps
IEEE 802.11g | 54Mbps, 2.4GHz standard backward compatible with 802.11b
IEEE 802.11n | Higher throughput using MIMO 54Mbps – 600Mbps 2.4GHz or 5GHz
IEEE 802.11h | DFS or Dynamic Frequency Selection & TPC Transmit Power Control 5GHz (Solves problems with interference Satellite.)
IEEE 802.11p | Wireless Access in Vehicular Environments or (WAVE) licensed ITS band of 5.9 GHz (5.85-5.925 GHz).

## Slide 5: Committee and Channel Width’s
 | Channel Width |  |  | 
Spatial Streams | 20 MHz | 40 MHz | 80 MHz | 160 MHz
1 | 86 Mbps | 200 Mbps | 433 Mbps | 866 Mbps
2 | 173 Mbps | 400 Mbps | 866 Mbps | 1.73 Gbps
3 | 288.9 Mbps | 600 Mbps | 1.3 Gbps | 2.34 Gbps
4 | 346.7 Mbps | 800 Mbps | 1.73 Gbps | 3.46 Gbp
Committee | Purpose
IEEE 802.11ac | Up to 1.3Gps per radio
Beam forming | Greater wireless AP/client link reliability
Multi-user MIMO | Greater AP/client capacity

## Slide 6: 2.4GHz 802.11b
Came alive in 1999
  Home
  Corporate Environments
Data shift rates
  11Mbps
  5.5Mbps
  2Mbps
  1Mpbs

## Slide 7: 2.4GHz 802.11b Range
1Mbps
2Mpbs
5.5Mbps
11Mbps
Ahhh!
Great signal

## Slide 8: 2.4GHz 802.11g
Came alive in 2003
  Backward compatible with 802.11b
  Gave us the 54Mbps data rate
  Will run at 802.11b rates in Mixed environment
Data shift rates
  54Mbps – 1Mbps Mixed environment
  We should disable 802.11b on our AP’s

## Slide 9: 2.4GHz 802.11g Range
1Mbps
2Mbps
5.5Mbps
6Mbps
9Mbps
11Mbps
54Mbps
Ahhh!
Great signal

## Slide 10: 2.4GHz 802.11n
Ratified in 1999
  Products appeared in market around 2001
  54Mbps
  28 non-overlapping channels
    23 of them available in U.S.
  Immune to 2.4GHz interference
    Microwave ovens
    Cordless phones
    Bluetooth devices

## Slide 11: Max Power Output limits for 2.4GHz
DSSS(CCK) | OFDM
100mW (-20dBm) | N/A
50mW(17dBm) | N/A
30mW(15dBm) | 30mW(15dBm)
20mW(13dBm) | 20mW(13dBm)
10mW(10dBm) | 10mW(10dBm)
5mW(7dBm) | 5mW(7dBm)
1mW(0dBm) | 1mW(0dBm)

## Slide 12: 2.4GHz 802.11a
Ratified in 2009
  Backward compatible with 802.11a/b/g
  Gives us up to 600Mbps data rate
  Allow for 8 antennas but most use 3
MIMO
  Uses Spatial Multiplexing
    Used when signals are received out of PHASE
  Maximal ratio combining (MRC)
    MRC only used when signals are received in PHASE
In todays wireless world this should be the minimum 802.11N

## Slide 13: 5GHz 802.11a
BAND | POWER MAX/EIRP MAX
UNII-1 Indoor Operations | 50mW(17dBm)/22dBm
UNII-2 Indoor or Outdoor Operations | 250mW(24dBm)/29dBm
UNII-3 Outdoor Bridge products | 1W(3dBm)/36dBm
UNII-1 & UNII-2 are used in U.S./ETSI channels: 36,40,44,48,52,56,60, and 64 | 
UNII-2 Extended channels: 100,104,108,112,116,120,124,128,132,136 and 140 these channels are an extension to the 802.11a that comes from the 802.11h standard | 

## Slide 14: 5GHz 802.11h
New Features | Definition
Dynamic Frequency Selection (DFS) | Monitors devices operating range for any radar signals that are allowed to operate within the 5GHz band. If it finds any it will abort the occupied channel or mark it as unavailable, to avoid INTERFERENCE.
Transmit Power Control (TPC) | You can fine tune the actual power transmitting the signal and maintain it within your WLAN.

## Slide 15: 5GHz 802.11b Speed and Distance
Chart: 
| 802.11b
11Mbps | 150
5.5Mbps | 160
2Mbps | 250
1Mbps | 350

## Slide 16: 5GHz 802.11g Speed and Distance
Chart: 
| 802.11g
54Mbps | 95
48Mbps | 100
36Mbps | 105
24Mbps | 150
18Mbps | 180
12Mbps | 202
9Mbps | 252
6Mbps | 300

## Slide 17: 5GHz 802.11a Speed and Distance
Chart: 
| 802.11a
54Mbps | 75
48Mbps | 90
36Mbps | 98
24Mbps | 130
18Mbps | 155
12Mbps | 165
9Mbps | 180
6Mbps | 200