## Slide 1: Layer 2 Switch Operations

## Slide 2: Switch Operations at layer 2
Shared media network uses the following:
  CSMA/CD
This is the problem
  Collisions occur constantly
  Half duplex operations
  Bandwidth is reduced

## Slide 3: Switch Operations layer 2
Layer 2 switching decisions about forwarding are based on destination MAC addresses
Ethernet switch provides isolation between connected hosts in several ways::
  The collision domain’s scope is severely limited
  Full duplex is now possible due to know contention media
  Errors in frames are not propagated, it uses the store-and-forward switching technology
  You can limit broadcast
  Other types of filtering or forwarding become possible

## Slide 4: Switch Operations layer 2
A layer 2 switch is basically a multiport transparent bridge.
  Each port is its own LAN segment
  Using the store and forward frame technology, switches will not forward any frame unless it knows the destination MAC address
  If it does not know the destination MAC address it will flood all other ports except the one it learned the source MAC from, in order to find the destination.
  This is called unknow unicast flooding
Several ways a switch can learn MAC address:
  Statically or Dynamically
  Sticky command comes into play

## Slide 5: Switch Operations layer 2
Decisions area made simultaneously by independent portions of switching hardware and be describes as follows:
  L2 forwarding table
  Security ACLs
  QoS ACLs
The CAM and TCAM table lookups have occurred, the frame is placed into the appropriate egress queue on the appropriate outbound switch port.