## Slide 1
IAS Assessor Training
US EPA ENERGY STAR®
Updated August 2020
Douglas Sickles, P.E.

## Slide 2
Accrediting Body Requirements
Requirements for assessing programs and scope
  EVERY ENERGY STAR® program requested by a laboratory MUST be assessed on initial assessment
    No sampling of programs
    Sampling of specific tests within a program is allowed
  For Surveillance
    Sampling may be acceptable
    Assessors should review for the most likely problem areas
  For Reassessment
    Every program must be assessed or reviewed

## Slide 3
Laboratory Requirements
Requirements
  Must achieve and maintain accreditation to ISO/IEC 17025:2017
  Develop and maintain procedures for each test method under the scope of accreditation (Data sheets if detailed enough can be considered procedures)
  Maintain records for EVERY test conducted on EVERY item tested
    Include observations and calculations
  Record every step required by ENERGY STAR® Program Requirements and/or 10 CFR 430 Subpart B, applicable Appendix

## Slide 4
Laboratory Requirements
Requirements
  Have a policy that sets out
    Quality objectives, commitments, and operational procedures
  Employ personnel that have the education and training to conduct tests
    Laboratory must establish specific requirements to identify minimum education and training
  Have the facilities and equipment necessary for the test
  Ensure equipment is accurate and calibrated, and records maintained
    Remember ISO/IEC 17025:2017 Clause 7.6.3 applies
    Calibration certificates must meet requirements of ISO/IEC 17025:2017 Clause 7.8.4

## Slide 5
Laboratory Requirements
Most critical equipment – Power meters
IEC 62301 – Household Appliances, Measurement of Standby Power
  Clause 4.4.1 - For measured power values of less than 1.0 W, the maximum permitted absolute uncertainty introduced by the power measurement equipment, Uma, shall be equal to or less than 0.02 W at the 95% confidence level. For >=1.0W, max relative uncertainty shall be = or < 2% measured power at 95%.
  Annex B, Clauses B.2.1, B.2.2
    a power resolution of 1 mW (0.001W) or better;
    an available current crest factor of 3 (or more) at rated range value;
    a minimum current range of 10 mA (or less);
    harmonic components up to at least 2.5 kHz (49th harmonic).
Check meter – often Yokogawa WT-series but can be others

## Slide 6
Conducting Assessments
Requirements
  Ethics
  Impartiality
  Confidentiality
  Undue influence
  Whistle Blower Protection Clause
  Program requirements and IAS requirements for assessors

## Slide 7
Conducting Assessments
Requirements
  Ethics must be reviewed
    EPA requires personnel participate in and regularly pass ethics and compliance audits
      “regularly” and “ethics/compliance audits” are not defined
      Customer organization should have a schedule and an approach to ethics
      Document the provisions that exist
  Impartiality evidence required
    Org chart shows all personnel free from influence
    Mechanisms for reporting/responding to attempts to exert undue influence on test results are in place
    Personnel are trained to recognize attempts at undue influence and steps to take
    17025:2017 Cl. 4.1.4 requires identifying risks to impartiality on an on-going basis. 4.1.5 requires demonstrating eliminating or minimizing those risks

## Slide 8
Conducting Assessments
Requirements
  Confidentiality - 17025:2017 Clause 4.2 requires:
    Legally enforceable commitments for management of information
    Customer notified in advance of any information placed in public domain; and notified of any released confidential information required by law
    Info about customer from source shall be confidential between customer and lab; source is confidential to lab and not shared with customer
    Specific steps taken to assure confidentiality must be reviewed
      Requirements in the Quality Manual
      Confidentiality agreements
      Review training provided to all personnel
    Document specific steps and actions implemented

## Slide 9
Conducting Assessments
Requirements
  Undue Influence
    Conditions and Criteria for Recognition of Laboratories for the ENERGY STAR® Program:
      Sec. 1f – “Maintain arrangements to ensure the freedom of laboratory management and personnel from any undue internal or external commercial, financial or other pressures and influences that may adversely affect the quality of their work.”
      Sec. 3 – “Notify EPA/DOE immediately of any attempt to hide or exert undue influence over test results.”
        This is also known as a “Whistleblower protection” clause
        This provision MUST be documented in the laboratory’s manual or similar level documentation

## Slide 10
Conducting Assessments
Requirements
  Implementing the “Whistleblower protection” provision
    Must be defined
    A log or similar system used to track any instances
    Personnel must be trained
      In the system
      How to recognize the attempts
  All the ethical issues discussed can create conflict of interest
    The laboratory must address conflict in the manual
    Personnel need to be trained
    Any conflicts need to be identified by all personnel
      Conflicts should be documented when identified

## Slide 11
Conducting Assessments
Requirements
  Assessors must
    Download the most current program requirement
      http://www.energystar.gov/products/spec
    Download and review 10 CFR 430 Subpart B, applicable Appendix
    Obtain and review any external documents referenced in the program requirements if possible
    Make sure the lab has in their scope the required test methods to be EPA Recognized for that product category. Check:
    Required Test Methods for EPA-recognized Laboratories (Non-Lighting – 3/10/20)
    ENERGY STAR Guide to EPA Laboratory Recognition by Lighting Category (Lighting – 11/2019)

## Slide 12
Conducting Assessments
Requirements
  Scope
    Other documents (e.g., ASTM, ASHRAE) may be listed to be included in the scope for industry needs
    Program requirements and/or 10 CFR 430 are needed for ENERGY STAR® specific scopes of accreditation
    If other standards, only the sections observed may be included on the scope, unless subsequent demonstration includes the entire standard
    IAS Scope may not need versions or dates of standards/criteria (Conditions and Criteria for Recognition of Laboratories for the ENERGY STAR® Program Clause 4 Note)
    Except for lighting, then requires dates, see EPA guide
      OK if client requests (sometimes 2 versions during transition)
      Each assessment we check they can do the latest version
      Usually no change in method, just stricter limits

## Slide 13
Conducting Assessments
Requirements for the IAS report/checklists
  List the specific programs desired and the programs observed
  If there are multiple tests and only some tests are observed, document those tests
  Document the specific item(s) observed in the demonstration
  Document the specific measures implemented for ethical requirements
    Including the last ethics training conducted
  Document whether the internal audit and management review included a review of the ethics training and protocols
  Document PT/ILC and any other steps taken to assure compliance to 17025 Clause 7.7
    Realize there may not be PT/ILC for that program or test

## Slide 14
Conducting Assessments
  Lead Assessor Checklists
    Main or Surveillance 17025 checklist must be used
    Supplemental ENERGY STAR® Quality Checklist must be used
      Most of this checklist relies on the 17025 checklist
  Technical Assessor Checklists
    General TAW can be used for ES scopes
      Specific checklists for Lighting, IES standards
      LM-79, LM-80 no longer required, obsolete

## Slide 15
Conducting Assessments
Requirements
  PT/ILC, aka Round Robin
    Requirement for ENERGY STAR® per EPA
      May not exist for the program
      May be impractical to have round robin for some programs
      Technical documentation must describe provisions to assure quality where round robin does not exist
        Refer to ISO/IEC 17025:2017 Clause 7.7
      When available, record PT number or similar control information, report date if the report is issued, and lab results (outlier or not)
  Reports from Challenge or Verification testing may fulfill the requirement, but must be examined

## Slide 16
Requirements for Lighting LM-79, LM-80
The lab shall:
  Periodically conduct checks between calibrations of the goniophotometer and integrating sphere systems.
  Conduct max 90 day checks using Reference standard lamps
  At least one of the checks will be the system calibration.
  Gonio and Sphere, max 12 month calibration.
  If the lab does their own calibration, they must have a procedure.
  Procedure shall include uncertainty influences, with MU at 95% confidence.
  If a change of components (e.g., power meter, detector) is necessary the system shall be recalibrated prior to use in testing. The uncertainty of the calibration shall be recalculated.
  LM-79 recently updated in 2019

## Slide 17
Acknowledgement
I have reviewed and understood the presentation and requirements outlined in this presentation.
______________________________________
  Insert an electronic signature onto the line above and e-mail back to IAS. As an alternative, this page may be printed and signed, and faxed or mailed back to IAS.