## Slide 1: Routing Protocol Overview

## Slide 2: Routing Protocols
Why do we use routing protocols?
Types of Routing Protocols
Two major types of Routing Protocols
  Distance Vector and Link State
Third Type would be
  Path Vector
  Uses multiple variable

## Slide 3: Routing Protocols
Another Category we could put Routing protocols in is:
  IGP or EGP
PROTOCOL | DV | LS | IGP | EGP | PV | AD
RIP | YES | no | YES | no | no | 120
EIGRP | YES | No | YES | no | no | 90/170
OSPF | no | YES | YES | no | no | 110/150
BGP | no | no | no | YES | YES | 20/200
IS-IS | no | YES | YES | no | no | 115

## Slide 4: Routing Protocols Specifics
RIP
  DV, Bellman-Ford Algorithm, Max Hop count is 15, Split horizon, poison reverse, Holddown Mechanisms, Supports CIDS, Multicast updates using the following IP4 address 224.0.0.9 or IP6 address FF02::9 to its neighboring router, MD5 authentication.
EIGHP
  Advanced Distance Vector, DUAL Algorithm, Max hop count is 255, default setting is 100, Based on Autonomous Systems 1-65535, creates a Topology Table, Routing Table and Neighbor Table, uses “K” values to help calculate best path, MD5 and SHA-2 authentication, Maintains anciencies using “hellos”, Other variables within the topology table, FS, SR and FD

## Slide 5: Routing Protocols Specifics
EIGRP
  Advanced Distance Vector, DUAL Algorithm, Max hop count is 255, default setting is 100, Based on Autonomous Systems 1-65535, creates a Topology Table, Routing Table and Neighbor Table, uses “K” values to help calculate best path, MD5 and SHA-2 authentication, Maintains anciencies using “hellos”, Other variables within the topology table, FS, SR and FD
Drawback of EIGRP
  Cisco Proprietary

## Slide 6: Routing Protocols Specifics
OSPF
  Link-State, Dijkstra Algorithm, No limitations, Based on Areas 0-4.2 billion, Creates a Topology Table, Routing Table and Neighbor Table, uses a process ID number to identify local database created 1-65535, OSPF authentication using key-chain, MD5 or authentication-key plain text or eight-character password. Also, OSPF uses LSA, SRO and LSU to create the local database.
  OSPF uses Back-Bone area, which is identified as the “zero” area. It also uses ABR or Area Border Routers what will communicate between different areas and ASBR or Autonomous System Border Router which communicates between different routing protocols to OSPF.

## Slide 7: Routing Protocols Specifics
OSPF continues
Stub area
  A stub area is an area that does not receive route advertisements external to the AS and routing from within the area is based entirely on a default route. An ABR deletes type 4, 5 LSAs from internal routers, sends them a default route of 0.0.0.0 and turns itself into a default gateway. This reduces LSDB and routing table size for internal routers.

## Slide 8: Routing Protocols Specifics
OSPF continues
Not so stubby area
  NSSA is an extension of the stub area feature that allows the injection of external routes in a limited fashion into the stub area. It visualizes the following activities: the ASBR imports external addresses with a type 7 LSA, the ABR converts a type 7 LSA to type 5 and floods it to other areas, the ABR acts as an "ASBR" for other areas. The ASBRs do not take type 5 LSAs and then convert to type 7 LSAs for the area.

## Slide 9: Routing Protocols Specifics
OSPF continues
DR and BDR
  OSPF in a Broadcast multiaccess or Multiaccess Network Segment, generates an election for the purposes of controlling the flow of traffic.
  The election process uses the following
    Highest IP address on any physical Interface
    Highest Loopback IP address
    Highest Priority number
  The above criteria are for electing the DR router.
  The BDR would use the same criteria, but it will be the second highest.

## Slide 10: Routing Protocols Specifics
OSPF continues
OSPF goes through 7 different states before convergence happens:
  Down: no OSPF neighbors detected at this moment.
  Init: Hello packet received.
  Two-way: own router ID found in received hello packet.
  ExStart: master and slave roles determined. (highest RID is master)
  Exchange: database description packets (DBD) are sent.
  Loading: exchange of LSRs (Link state request) and LSUs (Link state update) packets.
  Full: OSPF routers now have an adjacency..

## Slide 11: Routing Protocols Specifics
GBP
  Designed to exchange routing and reachability information among AS's on the internet. It makes decisions based on paths, network policies, rule-sets which are configured by a True Engineer
  iBGP is used for routing within an AS
  eBGP is the internet application of the protocol
  BGP creates "Peers" with its directly connected routers or not
BGP uses a Finite State Machine (FSM) in order to make decisions in its operations. The following are the Six states FSM uses:
  Idle, Connect, Active, OpenSent, OpenConfirm, Established

## Slide 12: Routing Protocols Specifics
GBP Continues
Idle State
  Refuse all incoming BGP connections.
  Start the initialization of event triggers.
  Initiates a TCP connection with its configured BGP peer.
  Listens for a TCP connection from its peer.
  Changes its state to Connect.
  If an error occurs at any state of the FSM process, the BGP session is terminated immediately and returned to the ldle state. Some of the reasons why a router does not progress from the ldle state are:
    TCP port 179 is not open.
    A random TCP port over 1023 is not open.
    Peer address configured incorrectly on either router.
    AS number configured incorrectly on either router.

## Slide 13: Routing Protocols Specifics
GBP Continues
Connect State
  Waits for successful TCP negotiation with peer.
  BGP does not spend much time in this state if the TCP session has been successfully established.
  Sends Open message to peer and changes state to OpenSent.
  It an error occurs, BGP moves to the Active state. Some reasons for the error are:
    TCP port 179 is not open.
    A random TCP port over 1023 is not open.
    Peer address configured incorrectly on either router.
    AS number configured incorrectly on either router.

## Slide 14: Routing Protocols Specifics
GBP Continues
Active State
  If the router was unable to establish a successful TCP session, then it ends up in the Active state.
  BGP FSM tries to restart another TCP session with the peer and, if successful, then it sends an Open message to the peer.
  If it is unsuccessful again, the FSM is reset to the Idle state.
  Repeated failures may result in a router cycling between the ldle and Active states. Some or the reasons for this include:
    TCP port 179 is not open.
    A random TCP port over 1023 is not open.
    BGP configuration error.
    Network congestion.
    Flapping network interface.

## Slide 15: Routing Protocols Specifics
GBP Continues
OpenSent State
  BGP FSM listens for an Open message from its peer.
  Once the message has been received, the router checks the validity of the Open message
  If there is an error it is because one of the fields in the Open message does not match between the peers, e.g., BGP version mismatch, the peering router expects a different My AS, etc. The router then sends a Notification message to the peer indicating why the error occurred.
  If there is no error, a Keepalive message is sent, various timers are set, and the state is changed to OpenConfirm.

## Slide 16: Routing Protocols Specifics
GBP Continues
OpenConfirm State
  The peer is listening for a Keepalive message from its peer.
  If a Keepalive message is received and no timer has expired before reception of the Keepalive, BGP transitions to the Established state.
  If a timer expires before a Keepalive message is received, or if an error condition occurs, the router transitions back to the ldle state.

## Slide 17: Routing Protocols Specifics
GBP Continues
Established State
  In this state, the peers send Update messages to exchange information about each route being advertised to the BGP peer.
  If there is any error in the Update message then a Notification message is sent to the peer, and BGP transitions back to the ldle state.

## Slide 18: Routing Protocols Specifics
IS-IS
  Developed by the ISO, uses the DIJKSTRA algorithm, NOT BASED ON IP
  IS-IS Is based on connectionless network service (CLNS) between routers
  It is a Layer 2 routing protocol
Integrated is-is supports IPv4 and IPv6
Level 1 routing: within an area (interior area)
  Can't talk to level2
  Different databases
Level 2 routing: between areas (backbone router)
Level 1-2 routing: like (ABR
Routers belong to areas not interfaces, such as OSPF
The interfaces on an is-is router do not need to be in both areas.

## Slide 19: Routing Protocols Specifics
IS-IS
  NSAP address(network service access point)
  Example: 49.0001.1111.1111.1111.00
AFl(authority and format id) set to 49: private use only
AREA ID: must be at least one byte
SYSTEM ID: defines an end system or int-sys in an area 48bits or 6bytes
NSEL (nsap selector) always 00 for IS-IS router for routing