## Slide 1: Troubleshooting OSPf

## Slide 2: OSPF Review
OSPF routing protocol is a link state routing protocol
Term | Definition
LSDB | The data structure held by an OSPF router for the purpose of storing topology data
SPF | The name of the algorithm OSPF uses to analyze the LSDB
LSU | The name of the OSPF packet that holds the detailed topology information
LSA | The name of class of OSPF data structure that hold topology information
Area | Contiguous grouping of routers and router interface
Backbone Router | Any router that has at least on interface connected to area 0
Internal Router | A router that has interface connected to only one area, making the router on the data link to perform special functions
BDR | A router on mult-access data link that monitors the DR and becomes prepared to take over for the DR, if it fails.

## Slide 3: OSPF Review
Uses Cost
Uses a Process ID Number
Configurations include
  Single area and Multi-Area
Uses Designated Routers and Backup Designated Routers

## Slide 4: All about OSPF
No limitation on routers
Does not summarize automatically
Uses Hello and Dead timers
Creates the following tables
  Routing table
  Neighbor table
  Database table

## Slide 5: Requirements to create Neighbors
Requirement | Yes/No
Interfaces primary IP addresses must be in same subnet | Yes
Must not be passive on the connected interface | Yes
Must be in same area | Yes
Hello and Dead timers must be the same | Yes
Router ID must be unique | Yes
Must pass neighbor authentication (Optional) | Yes
K-values must match | N/A

## Slide 6: Verifying OSPF
Command | Definition
Sh ip ospf int brief | Lists the interfaces on which OSPF is enabled, omitting passive interfaces
Sh ip protocols | List the contents of the network configuration commands for each routing process and a list enabled but passive interfaces
Sh ip ospf neighbor | List of known neighbors, including neighbor state.
Sh ip ospf database | List all LSAs for all connected area
Sh ip route | List the contents of the IP routing table.

## Slide 7: Common issues with ospf
Interface is down
Interface not running ospf process
Mismatched timers
Mismatched areas
Mismatched area type: stub or nssa
Different subnets
Passive interface: Once again don’t do it
Mismatched authentication
Acl
Mtu mismatch
Duplicate routers id